## Slide 1: Vmat radiotherapy planning head & Neck cancer
Zulaikha Jamalludin, PhD
Senior Lecturer / Clinical Oncology Physicist
University of Malaya Medical Centre

## Slide 2: disclosure
I Have NO Financial Or Non-financial Relationships In The Products Described, Reviewed, Evaluated Or Compared In This Presentation

## Slide 3: IMRT/VMAT
IMRT/VMAT is an advanced form of 3DCRT
The intensity of radiation beam is modulated/changed/adapted to:
  Match the target contour/shape – increased the dose conformality to the target
  Produce gradient of dose in surrounding normal tissues – minimizing dose to nearby organs at risk
Modulated intensity enable with advancement in:
  Dynamic Multi-leaf collimator design – changing speed with gantry movement
  Planning algorithm – inverse planning

## Slide 4: IMRT/VMAT
With IMRT/VMAT – possible to escalate the target dose while reducing the normal tissue doses
Unlike 3DCRT, the modulated intensity delivered to PTV with IMRT generate regions of high and low absorbed dose
Dose evaluation and reporting in IMRT evolved from previous ICRU for 3DCRT – attempt to retain a relationship with previous one

## Slide 5: ICRU: 3dCRT ‘vs’ imrt
3DCRT
Single point dose specification, ICRU ref point
Uniform dose distribution
Low dose gradient
D min = minimum absorbed dose
D max = maximum absorbed dose
IMRT/VMAT
Volume-based dose specification, D50%, median absorbed dose
Non-uniformity dose distribution
High dose gradient
D near-min = D98%
D near-max = D2%

## Slide 7: Planning aim: 3dCRT ‘vs’ imrt
3DCRT
Dose coverage aim: 95% isodose
Dose evaluation: 100%
Plan Dmax: < 107%
Dmax point location: less evaluation
Dose gradient: less evaluation
Irradiated volume: less evaluation
IMRT/VMAT
Dose coverage aim: 100% isodose
Dose evaluation: 98%, 95%
Plan Dmax: < 110%
Dmax point location: critical evaluation
Dose gradient: should give attention
Irradiated volume: should give attention

## Slide 8: cb-chop
C
Contours:
Review target volumes and OARS
B
Beam Arrangements/Fields:
Appropriate and reasonable
C
Coverage:
Evaluate on graphic plan and DVH
H
Heterogeneity/Hot Spots:
Value and location
O
Organs at Risk:
Review specified constraints, corresponding isodose lines on plan, and DVH
P
Prescription:
Total dose, dose per fraction, and image guidance

## Slide 9: Plan evaluation 1. Dose tolerance

## Slide 10: Dose tolerance protocol
Follow set of organs tolerance constraint – institutional protocol
  QUANTEC
  RTOG 0615
  Combination

## Slide 11
Serial organs that must be prioritized over target coverage
Serial organs that must be delineated, but not necessarily prioritized over target coverage
Organs at risk with some evidence for sparring, with serious but manageable toxicity
Poor evidence, uncertain endpoints or manageable toxicity.

## Slide 12: Plan evaluation 1. Dose evaluation

## Slide 13
Brainstem
Optic chiasm
Spinal cord
'BOchS'
Serial organs that must be prioritized over target coverage
What to evaluate?
Dmax = maximum dose

## Slide 14
  Dmax: From dose statistic - DVH
Serial organs that must be prioritized over target coverage

## Slide 15
  Dmax: From axial slice
    Find slice with max dose isodose line touching the organ
    Evaluate the isodose gradient (steep vs non-steep)
    Determine if need to reduce more without compromising coverage
Organs of critical importance that must be prioritized over target coverage

## Slide 16
Brainstem
Optic chiasm
Spinal cord
'BOchS'
Serial organs that must be prioritized over target coverage
What to evaluate?
DG = dose gradient
Dose gradient evaluation
As ‘Sharp’ As Reasonably Achievable – AShARA
AShARA
100% to 70% dose distance
85% to 70% dose distance (0.3-0.6)
85% to 50% dose distance (1.2-1.7)

## Slide 17
Optic nerve
Temporal lobe
PTV
'OnTeloPT'
Serial organs that must be delineated, but not necessarily prioritized over target coverage
Serial organs - What to evaluate?
Dmax = maximum dose
DG = dose gradient

## Slide 18
Optic nerve
Temporal lobe
PTV
'OnTeloPT'
Serial organs that must be delineated, but not necessarily prioritized over target coverage
PTV - What do u want to know?
How much PTV volume covered by 100% dose? – V100%
What is the min dose covering 99%/all PTV volume? - D99%
PTV - What to evaluate?
Prescribed dose
Hot/Higher dose

## Slide 19
Optic nerve
Temporal lobe
PTV
'OnTeloPT'
Serial organs that must be delineated, but not necessarily prioritized over target coverage
PTV - What do u want to know?
Is it a HOT plan?
Where is the Dmax? - near/in BOchS?
PTV - What to evaluate?
Prescribed dose
Hot/Higher dose

## Slide 20
Ensure high doses island/hotspot small in size & away from any OARs (> 5mm)
  Hotspot exist as consequence of pushing dose in OARs
  Can be reduced & eliminated (if only 1 @ 2 OARs involved)
  Can be reduced slightly BUT Cannot eliminate it (if many OARs involved)

## Slide 21
Organs at risk with some evidence for sparring, with serious but manageable toxicity
Poor evidence, uncertain endpoints or manageable toxicity.
OARs mean dose - How to evaluate?
Dose gradient evaluation
ALARA concept – as low as reasonably achievable

## Slide 22: Dose gradient – cochlear
Axial view – Dose gradient
AShARA

## Slide 23: Dose gradient – cochlear

## Slide 24: Dose gradient – oral cavity
Axial view – 50% isodose line - PUSH
Coronal view – 50% isodose line - PUSH

## Slide 25: Dose gradient – larynx
Axial view:
  50% isodose line – ALARA
  NO 70% isodose line

## Slide 26: Dose gradient – constrictor muscle
Axial view:
  50% isodose line – ALARA
  NO 70% isodose line

## Slide 27: Dose gradient – post neck
Axial view:
  NO 50% isodose line
Sagittal view:
  NO 50% isodose line

## Slide 28: Dose gradient – post neck

## Slide 29: Dose gradient – parotid
Axial view – 30% isodose line - IN
Coronal view – 30% isodose line - IN

## Slide 30
Volumetric tolerance, V30Gy ≤ 45%
Dose calculation:
  (30Gy/70Gy)x100 = 43% isodose ~ 50% isodose
Volume calculation
  45% volume ~ 50% volume = ½ parotid volume
Ideally ~ 50% isodose line placed at ½ parotid volume

## Slide 32: Larynx case parotid 30% - ALARA

## Slide 33: Irradiated volume - reduce
  50% isodose line – ALARA
  70% isodose line – ALARA
  Dose Gradient –
  As ‘Sharp’ As Reasonably Achievable – AShARA

## Slide 34: parotid case unilateral 50% isodose - ALARA

## Slide 35: brain case – scalp 50% - ALARA

## Slide 36: brain case – scalp 50% - ALARA

## Slide 37: Npc imrt demand & supply

## Slide 38: Demand & supply in npc imrt
demand
No demand / Under-demand
  As long as achieve dose tolerance
  Experience-related
supply
No demand / under-demand
  As long as achieve dose tolerance
  Comfort zone
    No idea of how far the system can push
    Lack of understanding - Loose chance of plan quality improvement
(Oncologist)
(Physicist/Planner)
Over-demand
  Too ambitious – spare all, high dose
  Illogical/not deliverable
Over-demand
  Pushing the system
    Algorithm can be pushed – is it mechanically deliverable?

## Slide 39: Demand & supply in npc imrt
demand
supply
(Oncologist)
(Physicist/Planner)

## Slide 40: Once upon a time …. larynx 70% revisit (2016 vs current)

## Slide 41: Once upon a time …. Parotid 30% revisit (2016 vs current)

## Slide 42: Current rt considerations in npc

## Slide 43: Loosening 'BOchS' & 'OnTeloPT'dose ?

## Slide 44: Loosening 'BOchS' & 'OnTeloPT'dose ?

## Slide 45: Hypoglossal dose ?

## Slide 46: Take home messages…
Numbers of parameters taken into account to generate acceptable plan – physical paramaters, machine limitations & planner’s experience (knowledge & skills)
Common pitfall in training or practice is relying on plans generated without analysis & discussion on the produced plan - mistakes happen, and physicists/planners change with time and institution – upgrade in knowledge
Common to request a plan revision to improve target coverage or oar objective doses – generating a good plan is a teamwork process (physicists/planners & clinicians)
Demand & supply increase skills and experiences of both clinicians & physicists/planners

## Slide 47: TQ

## Slide 48
C
Contours:
Review target volumes and OARS
P
Prescription:
Total dose, dose per fraction, and image guidance
C
Coverage:
Evaluate on graphic plan and DVH
H
Heterogeneity/Hot Spots:
Value and location
O
Organs at Risk:
Review specified constraints, corresponding isodose lines on plan, and DVH
B
Beam Arrangements/Fields:
Appropriate & Reasonable
Check on total arcs numbers;
  Round TV = 1-2 arcs (2 arcs preferable – movement/physiological changes uncertainty)
  Long/Mass TV = 3-4 arcs
  Arcs length
Check on colli angle – opposite direction for optimum use (except Monaco)
Check on beam/tx deliverability
  Gantry hit couch? – couch kick plan and LT/RT isoc with full arc?
Rule of thumb for MU checking; MU Factor
  Total MU determined the complexity level of IMRT plan
  Less total MU = less modulation equal to open beam plan
  High total MU = increase modulation complexity
  Need to find optimum total MU = producing acceptable plan + pass QA + deliverable
  Total MU = Dose/# x MU factor 2-4 (min to max)
  Within MU factor 2-4 = acceptable beam complexity - pass QA

## Slide 49
60Gy/20# = 3Gy
300 cGy x 2 = total min 600 MU
300 cGy x 4 = total max 1200 MU
1115MU/300cGy = 3.7 MU factor
Total = 1115
70Gy/33# = 2.121Gy
212 cGy x 2 = total min 424 MU
212 cGy x 4 = total max 848 MU
578MU/212.1cGy = 2.7 MU factor
Total = 578